## Slide 1: BRAIN COMPUTER INTERFACE
Presented by
Sandhra anna jerry

## Slide 2: Introduction
Brain-computer interface (BCI) is a collaboration between a brain and a device that enables signals from the brain to direct some external activity, such as control of a cursor or a prosthetic limb.
The interface enables a direct communications pathway between the brain and the object to be controlled.
By reading signals from an array of neurons and using computer chips and programs to translate the signals into action, BCI can enable a person suffering from paralysis to write a book or control a motorized wheelchair or prosthetic limb through thought alone.

## Slide 3
BCIs are often directed at researching, mapping , assisting, augmenting , or repairing human cognitive or sensory-motor functions.
Implementations of BCIs range from non-invasive (EEG , MEG , EOG , MRI) and partially invasive (ECoG and endovascular) to invasive (microelectrode array), based on how close electrodes get to brain tissue.
Recently, studies in human-computer interaction via the application of machine learning to statistical temporal features extracted from the frontal lobe (EEG brainwave)data has had high levels of success in autonomous recognition of fall detection as a medical alarm , mental state (Relaxed, Neutral, Concentrating), mental emotional state (Negative, Neutral, Positive) and thalamocortical dysrhythmia.

## Slide 4: BCI functions
Applications of Brain Computer Interface bases its functionality on either observing the user state or allowing the user to deliver his⧹⧹her ideas.
BCI system records the brain waves and sends them to the computer system to complete the intended task. The transmitted waves are therefore used to express an idea or control an object.
Communication and control
Brain computer interface (BCI) systems build a communication bridge between human brain and the external world eliminating the need for typical information delivery methods.
They manage the sending of messages from human brains and decoding their silent thoughts. Thus they can help handicapped people to tell and write down their opinions and ideas via variety of methods such as in spelling applications , semantic categorization , or silent speech communication.

## Slide 5
2. User State Monitoring
Early BCI applications have targeted disabled users who have mobility or speaking issues.
Their aim was to provide an alternative communication channel for those users. But later on, BCI enters the world of healthy people as well. It works as a physiological measuring tool that retrieves and uses information about an individual’s emotional, cognitive or affectiveness state.
The target of brain signals utilization has been extended beyond controlling some object or offering a substitution for specific functions, in what is called passive BCI .
BCI User state monitoring function is considered a helpful hand in Human Computer Interfaces and adapts them according to the estimated user emotional or cognitive state.
It also contributes in the development of smart environments and emotion controlling applications .

## Slide 6: Bci applications
1. Medical applications
Healthcare field has a variety of applications that could take advantage of brain signals in all associated phases including prevention, detection, diagnosis, rehabilitation and restoration .

## Slide 7
1.1 Prevention
Various consciousness level determination systems along with their brain-related studies have been developed.
The attentiveness influences of smoking and alcohol on brain waves have been enlightened. The importance of such studies for medical prevention lies in the possible loss of function and decrease of alertness level resulting from smoking or alcohol drinking.
Traffic accidents are considered the main cause for death or some serious injuries as claimed.Analyzing their causes for later prevention has been a concern for researches in various fields.
Thus concentration level for those suffer from motion sickness, especially drivers, has been studied. Motion sickness, which occurs as a result of sending conflicted sensory information generated from body, inner ear and eye to the brain, is usually happening on moving transportation media. It can cause traffic accidents as it declines in a person’s ability to maintain self-control.
And prediction of motion sickness could contribute in a driver-state monitoring and alertness system using a set of EEG power indicators. Its accompanying EEG signals from different five brain regions have been examined. The human hearing level, as part of sensory information gathering process, has been measured via auditory evoked potential BCI-based system .
In another study , a virtual reality-based motion-sickness platform has been designed with a 32-channel EEG system and a joystick which is used to report the motion sickness level (MSL) in real time experiments. Consciousness level monitoring via brain waves has been expanded to include not only drivers but also stayed-alone sick people as suggested .

## Slide 8
1.2 Detection and diagnosis
Mental state monitoring function of BCI systems has also contributed in forecasting and detecting health issues such as abnormal brain structure (such as brain tumor) , seizure disorder (such as epilepsy), sleep disorder (such as narcolepsy), and brain swelling (such as encephalitis).
Tumor , which is generated from uncontrolled self-dividing of cells, could be discovered using EEG as a cheap secondary alternative for MRI and CT-SCAN. EEG-based Brain tumor detection systems have been the main subject of the Researches.
1.3 Rehabilitation and restoration
Mobility rehabilitation is a form of physical rehabilitation used with patients who have mobility issues, to restore their lost functions and regain previous levels of mobility or at least help them adapt to their acquired disabilities .
People suffer from serious injuries or events such as strokes may also be able to fully recover.
Stroke is a condition in which the brain cells suddenly die because of the lack of oxygen. It can be caused by an obstruction in the blood flow . Disabilities and brain strokes have been subject for many studies interested in solutions involving brain signals.
It has been pointed out that brain structures associated with stroke injuries could be reorganized and the damaged motor functions could be restored via neuroplasticity .
For patients who cannot recover previous levels of mobility or communication, BCI based prosthetic limbs, also called neuroprosthetic devices, can be used to regain normal functionality

## Slide 9
2. Neuroergonomics and smart environment
Smart environments such as smart houses, workplaces or transportations could also exploit brain computer interfaces in offering further safety, luxury and physiological control to humans’ daily life. They are also expected to witness cooperation between Internet Of Things (IOT) and BCI technologies.
Brain computer interface-based Smart Living Environmental Auto-adjustment Control System (BSLEACS)- It monitors user’s mental state and adapts the surrounding components accordingly. It has extended its functionality with the involvement of universal plug and play (UPnP) home networking.
Brain signals also assist in improving workplace conditions by assessment of an operator’s cognitive state .
They also analyze the impact of workload mental fatigue and task time on EEG features . Operating room as well represents a candidate place for smart workplace BCI-based application .
The field of intelligent transportation has also been benefitted from the cognitive state monitoring BCI function. Driver’s behavior has been studied in numerous studies. It has been found that distraction and fatigue are two main sources for driver’s inattention, which is considered as a strong cause for most traffic accidents.

## Slide 10
3. Neuromarketing and advertisement
Marketing field has also been an interest for BCI researches.
Research has explained the benefits of using EEG evaluation for TV advertisements related to both commercial and political fields. BCI based assessment measures the generated attention accompanying watching activity .
On the other hand, the researchers have considered the impact of another cognitive function in neuromarketing field. They have been interested in estimating the memorization of TV advertisements thus providing another method for advertising evaluation.

## Slide 11
4. Educational and self-regulation
Neurofeedback is a promising approach for enhancing brain performance via targeting human brain activity modulation.
It invades the educational systems, which utilizes brain electrical signals to determine the degree of clearness of studied information. Personalized interaction to each learner is established according to the resultant response experienced .
Learning to self-regulate through non-invasive BCI has also been studied. It provides a mean for improving cognitive therapeutic approaches.

## Slide 12
5. Games and entertainment
Entertainment and gaming applications have opened the market for non medical brain computer interfaces. Various games are presented like ,where helicopters are made to fly to any point in either a 2D or 3D virtual world.
Combining the features of existing games with brain controlling capabilities has been subject to many researches which tend to provide a multi-brain entertainment experience.
6. Security and authentication
Security systems involve knowledge based, object based or biometrics based authentication.
They have shown to be vulnerable to several drawbacks such as simple insecure password, shoulder surfing, theft crime, and cancelable biometrics .
Cognitive Biometrics or electrophysiology , where only modalities using biosignals (such as brain signals) are used as sources of identity information, gives a solution for those vulnerabilities.
The motivation behind exploring the feasibility of electrophysiology is that biosignals cannot be casually acquired by external observers. They also can be of great value for disabled patients or users missing the associated physical trait .This makes such signals difficult to synthesize and therefore improves the resistance of biometric systems to spoofing attacks.

## Slide 13: BCI system components
BCI system consists of four basic components.
They include signal acquisition, signal preprocessing, feature extraction, and classification.
Signal acquisition component, is responsible for recording the brain waves and sending them to the preprocessing component for signal enhancement and noise reduction.
Feature extraction component generates the discriminative characteristics for the improved signal, decreasing the size of the data applied to the classification component.
Classifiers are translating the produced features into device commands.

## Slide 14: Challenges faced
Establishing the communication interface using brain signals has faced a lot of challenges. They can be categorized as technical and usability.
Technical challenges are concerned with the system obstacles specially those regarding EEG features characteristics. Usability challenges describe the limitations affecting the level of human acceptance .
1.Usability challenges
They express the limitations facing the user acceptance of BCI technology utilization . They include the issues related to the training process necessary for classes discrimination.
Information Transfer Rate (ITR) is one of the system evaluation metrics that combines both performance and acceptance aspects.

## Slide 15
1. Training process
Training the user is a time-consuming activity either in guiding the user through the process or in the number of recorded sessions.
It takes place either in preliminary phase or in the classifier calibration phase . The user is taught to deal with the system as well as to control his or her brain feedback signals in the preliminary phase, while in the calibration phase, trained subject’s signal has been used to learn the used classifier.
2.Information Transfer Rate
It is the widely used evaluation metric for command BCI systems.
It depends on the number of choices, the accuracy of target detection, and the average time for a selection. Thus compared to imagery BCI, selective attention strategies achieve higher ITR as their offered choices are larger .

## Slide 16
Technical challenges
They are issues related to the recorded electrophysiological properties of the brain signals which include non-linearity, non-stationarity and noise, small training sets and the companying dimensionality curse.
1 Non-linearity
The brain is a highly complex nonlinear system in which chaotic behavior of neural ensembles can be detected.
Thus EEG signals can be better characterized by nonlinear dynamic methods than linear methods.
2 Nonstationarity and noise
Nonstationarity attribute of electrophysiological brain signals represents a major issue in developing a BCI system. It originates a continuous change of the used signals over time either between or within the recording sessions.
The mental and emotional state background through different sessions can contribute in EEG signals variability. Also fatigue and concentration levels are considered part of internal nonstationarity factors.

## Slide 17
Noise is also a big contributor in the challenges facing the BCI technology and causing the nonstationarity issue. It includes unwanted signals caused by alterations in electrode placement, and environmental noise.
3. Small training sets
The training sets are relatively small, since the training process is influenced by usability issues.
Although heavily training sessions are considered time consuming and demanding for the subjects, they provide the user with necessary experience to deal with the system and learn to control his or her neurophysiological signals.
Thus a significant challenge in designing a BCI is to balance the trade-off between the technological complexity of interpreting the user’s brain signals and the amount of training needed for successful operation of the interface.
4. High dimensionality curse
In BCI systems, the signals are recorded from multiple channels to preserve high spatial accuracy.
As the amount of data needed to properly describe different signals increases exponentially with the dimensionality of the vectors, various feature extraction methods have been proposed. They play an important role in identifying distinguishing characteristics.
Thus the classifier performance will be affected only by the small number of distinctive traits instead of the whole recorded signals that may contain redundancy.

## Slide 18: Proposed solutions
1. Noise removal
Preprocessing in either spatial, time or frequency domains has contributed in enhancing the signal caused especially by external factors.
Improving the signal to noise ration (SNR)of EEG signals is done by increasing the signal level and decreasing the noise level.
Frequency-band filtering assists in removing noise and artifact. It can also provide a significant help with handling the internal nonstationarity factors.
The task related frequencies can be selected to be used for further analysis in BCI systems.
2. Separability of multiple classes
Machine learning techniques are employed to translate user’s intent into a valid choice. They discriminate and identify the selected class.
They have been used, for example, to overcome some limitations associated with small training sets, single trial, and also the variability between sessions and within individual sessions. They also aim to achieve higher performance and accordingly, higher ITR results.